Wiring a K3 clock to a K1 bike

| K3 Naked Clock |  | K1 Wiring |
| --- | --- | --- |

| Pin number | Wire colour | Function/to | Colour | Pin number |
| --- | --- | --- | --- | --- |
| 1 | Red/White | Battery | Battery | Red | 1 |
| 2 | Orange/Green | Ignition Live | Ignition Live | Orange/Green | 2 |
| 3 | Orange/Red | Speed Sensor | Speed Sensor | Orange | 3 |
| 4*** | Brown/Black | ECM | Ignition Coil | Black/Yellow | 4 |
| 5 | Yellow/Black | Fuel Level | Fuel Level B | Light Green/Black | 5* |
| 6 | Green/Yellow | Oil Pressure Gauge | Fuel Level A | Red/Black | 6 |
| 7 | Empty | NOTHING | Oil Pressure Gauge | Green/Yellow | 7 |
| 8 | Black/White | Ground (Power) | Ground (Power) | Black/White | 8 |
| 9 | Orange/Green | Ignition Live | Clock Lights | Grey | 9** |
| 10 | Yellow | High Beam | High Beam | Yellow | 10 |
| 11 | Black | Turn Left | Turn Left | Black | 11 |
| 12 | Light Green | Turn Right | Turn Right | Light Green | 12 |
| 13 | Pink/White | Speed Sensor | Neutral Switch | Blue/Black | 13 |
| 14*** | Black/Green | ECM | Speed Sensor | Pink | 14 |
| 15 | Blue/Black | Neutral Switch | Water Temp Switch | Black/Green | 15 |
| 16 | Black/White | Ground (Power) | Ground (Signal) | Black/Brown | 16 |

ISSUES

- The clock (tells the time) resets it’s self every time ignition is switched off. Possibly the live wire on the K1 to the clock is not permanently live. Will have to source a new wire that is and take feed from that.

- The tacho needle goes haywire once the ignition is switched on. Possibly due to the fact that the tacho sensor wires on the K3 goes to the ECM unit before returning to the front of the bike and then into the clock. I assume that there is a bit of electronic wizardry going on in the ECM.

- The check light comes on when the ignition is switched on but stays on permanently.

- There is no water temperature display.

*Only one of these wires is used (which one is up to you). K3 clock only has 1 fuel light warning rather than the 2 that the older model has.

**On the K1 clock pin 9 (grey) is not used for the morphing of the K3 clock. As clock lights will illuminate with the ignition on position.

*** Pin 4 & 14 on the clock are not used as the older model does not have an ECM unit.

NOTE: Some, but not all, of the wires are a direct connection from the clock to the loom. I have done enough of the correct wiring to get the speedometer, all warning lights and indicating lights to function. If anyone does better than I have so far then please let me know.